## Slide 1: EXPLORING SPECTRAL INDICES IN Google Earth Engine (CERSGIS)

## Slide 2: OVERVIEW
Spectral Indices are combinations of spectral reflectance from two or more wavelengths that indicate the relative abundance of features of interest
There are different indices for vegetation, built-up features, water and burned areas
In this section we will have hands-on tutorial exploring some vegetation indices in the Google Earth Engine environment.

## Slide 3: Importing Image and Feature Collections
Import the Landsat 8 Surface Reflectance collection as well as the Study Area
Visualize area of interest and centre visualization to your area of interest
Notes: Landsat scenes with the highest available data quality are placed into Tier 1. They are precise, terrain and radiometry corrected, and inter-calibrated across the different Landsat Instruments.

## Slide 4: Cloud Masking
Cloud information stored in the pixel_qa band
Cloud flags are based on the CFMASK algorithm
Clouds and cloud shadows are screened out at all confidence levels
Zhu, Z., & Woodcock, C. E. (2012). Object-based cloud and cloud shadow detection in Landsat imagery Remote sensing of environment, 118, 83-94.

## Slide 5: Cloud Masking
FMASK implements a rule‐based algorithm
Initial spectral test to identify cloud pixels
Determine cloud probability based on brightness and temperature
Identify potential cloud shadows using a flood‐fill test based on the NIR band
Estimate cloud height (based on temperature) and identify the shadow associated with each cloud object

## Slide 6: Cloud Masking
Set up the Cloud Masking Function

## Slide 7: Filtering an ImageCollection
Build image composite with;
filterBounds()
filterDate()
filterMetadata(cloud cover)
Map to the cloud mask
Reducer, median()
Clip to area of interest
Visualization of the image composite in false colour.

## Slide 8: Calculating NDVI
Calculate the NDVI using the normalizedDifference() method.
The normalized difference is computed as (NIR – Red) / (NIR + Red)
NIR is band 5, and red is band 4.
NDVI output of Study Area

## Slide 9: Tasseled Cap Transformation
Tasseled Cap Transformation is a method to transform spectral information of satellite data into spectral indicators, useful for vegetation analysis
Provides an analytical way to detect and compare changes in vegetation, soil, and man-made features over time
Coefficients used in the linear equation of Tasseled Cap transformation are sensor specific
The first three bands created are generally held to represent
  Brightness: measured value for the ground
  Greenness: measured value for vegetation
  Wetness: measured value for canopy moisture

## Slide 10: Tasseled Cap Transformation
Derivation of the three levels of information for Landsat is a weighted sum of the bands (without the thermal channel 6), where each band is multiplied by its specific coefficient:
Brightness = 0.3037 (band 2) + 0.2793 (band 3) + 0.4743 (band 4) + 0.5585 (band 5) + 0.5082 (band 6) + 0.1863 (band 7)
Greenness = −0.2848 (band 2) − 0.2435 (band 3) − 0.5436 (band 4) + 0.7243 (band 5) + 0.0840 (band 6) − 0.1800 (band 7)
Wetness = 0.1509 (band 2) + 0.1973 (band 3) + 0.3279 (band 4) + 0.3406 (band 5) − 0.7112 (band 6) − 0.4572 (band 7)
References:
Benefoh, D. T., et al (2018). Assessing land-use typologies and change intensities in a structurally complex Ghanaian cocoa landscape. Applied Geography, 99, 109-119
Crist, E. P., & Kauth, R. J. (1986). The Tasseled Cap de-mystified.[transformations of MSS and TM data

## Slide 11: Tasseled Cap Brightness (TC-B)
Generating the three tasseled cap bands the same way as done in Benefoh et al., 2018 using the bands; Blue, Green, Red, Near Infrared and the Shortwave Infrared bands of Landsat
Tasseled Cap Brightness output of study area

## Slide 12: Tasselled Cap Greenness (TC-G)
Compute for tasseled cap greenness in GEE
Tasseled Cap Greenness output of Study Area

## Slide 13: Tasselled Cap Wetness (TC-W)
Compute for tasseled cap wetness using derived coefficients for Landsat data
Tasseled Cap Wetness output of study area

## Slide 14: Land Surface Water Index (LSWI)
Calculate the LSWI using the normalizedDifference() method.
The normalized difference is computed as (NIR – SWIR1) / (NIR + SWIR1)
NIR is band 5
Shortwave infrared 1 is band 6.
LSWI output of study area

## Slide 15
Link to GEE script
https://code.earthengine.google.com/0a82390c4dcc0f581bd0fbd9573057ef

## Slide 16: Hands-on Exercises
Using Sentinel-2 MSI: Multispectral Instrument, Level-1C Image Collection, compute the following indices in Google Earth Engine. Use geometry Point(0.03695166,7.12756658) as point of interest.
Normalized Difference Water Index (NDWI)
Normalized Difference Built-up Index (NDBI)
Enhanced Vegetation Index (EVI)

## Slide 17: Thank You
Notes: It's free for non-commercial use!